Boost Adjuster Bleed Valve Installation Guide

Tel: 01531 650350 email: sales@allisport.com

AlliSport Ltd, HR8 1RZ

# Text boxes

ACTUATOR

6mm rubber

pipe

Tee piece

Supplied

Insert Tee into rubber pipe

TURBO COMPRESSOR

Nylon Pipe supplied

Bleed Valve

We are aiming to achieve maximum boost under load of no more than 14psi. (1 bar)

A good indication of correct boost is the red turbo light on the instrument panel will illuminate under full load when hot.

To Atmosphere